Press release

ATE PowerDisc: Major extension of product range announced

- High-performance brake discs will be available for even more vehicles starting in the third quarter of 2015

- Multifunctional groove increases braking power

- Quick installation and sporty look

Frankfurt, May 21, 2015. Starting in the third quarter of this year, the ATE PowerDisc will be available for even more vehicles. ATE will add 65 article numbers, increasing its coverage by about 50 percent. This high-performance product enables increased braking power on both wet and dry road surfaces. A multifunctional “infinite loop” groove on the brake disc diverts moisture, gases and dirt that can reduce braking performance, and it looks good as well. Fading, which can be caused by escaping gas, is prevented.

Quick installation in repair shops – high performance and sporty look for drivers

Another advantage of the PowerDisc is that it is supplied with corrosion protection. This not only extends the service life of the brake disc, it also means that no cleaning is required before installation. Repair shops can thus install them more quickly. In addition, wear tests are more effective: the depth of the multifunctional groove is also the minimum thickness of the brake disc. Mechanics can therefore see if a disc has reached its wear limit without dismantling the brake or using measuring tools. As long as the groove is visible, the wear limit has not been reached.

The extension of the PowerDisc line will give repair shops a larger and more attractive range of brakes for drivers who value high performance and a sporty appearance.

For details on the vehicles covered and the necessary General Operating Permit for the ATE PowerDisc, visit www.ate-brakes.com.

Continental develops intelligent technologies for transporting people and their goods. As a reliable partner, the international automotive supplier, tire manufacturer, and industrial partner provides sustainable, safe, comfortable, individual, and affordable solutions. In 2014, the corporation generated sales of approximately €34.5 billion with its five divisions, Chassis & Safety, Interior, Powertrain, Tire, and ContiTech. Continental currently employs approximately 200,000 people in 53 countries.

Information management in and beyond the vehicle is at the very heart of the Interior division. The product portfolio for different types of vehicles includes: instrument clusters, multifunctional and head-up displays, control units, access control and tire-information systems, radios, infotainment systems, input devices, control panels, climate control units, software, cockpits as well as services and solutions for telematics and Intelligent Transportation Systems. The Interior division employs more than 36,000 people worldwide and generated preliminary sales of approximately €7 billion in 2014.

Within the Interior Division the Commercial Vehicles & Aftermarket Business Unit accommodates the specific requirements of the commercial vehicle, special vehicle and aftermarket sector. A global network of sales and service companies ensures proximity to local customers. Covering the product brands Continental, VDO, ATE, Galfer and Barum the Business Unit offers electronic products, systems and services for commercial and special vehicles, a broad selection of products for specialized workshops and spare parts for the Independent Aftermarket and the Original Equipment Services after end of series production of the vehicle manufacturer.

Contact for Journalists

Frederick Wilde

Media Relations and Internal Communications
Commercial Vehicles & Aftermarket

Continental

Phone: +49 69 7603-9406
E-Mail: Frederick.Wilde@continental-corporation.com

This press release is available in the following languages: German, English

Links

Online press portal: www.continental-presse.de www.continental-presse.de

Media database: www.continental-mediacenter.com

Video portal: videoportal.continental-corporation.com